| Steven L. Beshear Governor | Energy and Environment Cabinet Department for Environmental Protection Division of Water 200 Fair Oaks Lane 4th Floor Frankfort, Kentucky 40601 Phone: (502) 564-3410 Fax: (502) 564-2741 www.water.ky.gov | Leonard K. Peters Secretary R. Bruce Scott Commissioner |
| --- | --- | --- |

KENTUCKY LABORATORY CERTIFICATION PROGRAM

Kentucky KPDES Permit Defined Total Nitrogen (Nitrogentotal) Determination

Kentucky Division of Water Permitting Section has defined Nitrogen (total) as a state-defined parameter in 401 KAR 10:031 and individual permits.  Kentucky wastewater laboratories seeking certification for Nitrogen (total) to meet KPDES permit defined parameter may utilize the following scenarios:

Nitrogen (total) is defined as the sum of Total Kejeldahl Nitrogen, nitrate and nitrite.

[Nitrogentotal] = [TKN] + [NO3-] + [NO2-]

Laboratories may select any one of the following three options:

Option #1.	Analyze TKN, nitrate and nitrite using EPA and KY approved wastewater methods listed in 40 CFR 136.  Add the results (using the same units) to obtain Nitrogen (total) as follows:

[Nitrogentotal] = [TKN] + [NO3-] + [NO2-]

Laboratories utilizing Option #1 must submit the following to DOW:

| Method | PT | IDC | MDL | SOP | EPA Method1 | Regional ATP Request2 |
| --- | --- | --- | --- | --- | --- | --- |
| TKN | X | X | X | X | N/A | N/A |
| [NO3-] | X | X | X | X | N/A | N/A |
| [NO2-] | X | X | X | X | N/A | N/A |

1.  Analytical method written using EPA standard format.

2.  Regional ATP Request to DOW following procedure specified in 40 CFR 136.5.

X = Required.

N/A = Not applicable.

Option #2.	Analyze TKN, nitrate/nitrite using EPA and KY approved wastewater methods listed in 40 CFR 136.  Add the results (using the same units) to obtain Nitrogen (total) as follows:

[Nitrogentotal] = [TKN] + [NO3-]/[NO2-]

Laboratories utilizing Option #2 must submit the following to DOW:

| Method | PT | IDC | MDL | SOP | EPA Method1 | Regional ATP Request2 |
| --- | --- | --- | --- | --- | --- | --- |
| TKN | X | X | X | X | N/A | N/A |
| [NO3- + NO2-] | X | X | X | X | N/A | N/A |

1.  Analytical method written using EPA standard format.

2.  Regional ATP Request to DOW following procedure specified in 40 CFR 136.5.

X = Required.

N/A = Not applicable.

Option #3.	Utilize Hach Method TNT plus 880 (10242) simplified method (s-TKN) for the measurement of total Kjeldahl nitrogen (TKN) and Hach method Nitrate/Nitrite (10206).  Nitrate/Nitrate (10206) is included in TNT plus 880 (10242) (Figure 1).

s-TKN is defined as TKN = [Nitrogentotal] - [NO3- / NO2-]

And by substitution,

[Nitrogentotal] = [TKN] + [NO3- / NO2-]

Figure 1:  Hach Method TNT plus 880 for use in determining Nitrogen (total) and Nitrate/Nitrite.

Laboratories utilizing Option #3 must submit the following to DOW:

| Method | PT | IDC | MDL | SOP | EPA Method1 | Regional ATP Request2 |
| --- | --- | --- | --- | --- | --- | --- |
| s-TKN (Hach 10242) | X | X | X | X | X | X |
| [NO3- + NO2-] (Hach 10206) | X | X | X | X | X | X |

1.  Analytical method written using EPA standard format.

2.  Regional ATP Request to DOW following procedure specified in 40 CFR 136.5.

s-TKN Method Quality Assurance/Quality Control (QA/QC) Requirements

| QA/QC Parameter | Analyte(s) | Frequency | Acceptance Criteria |
| --- | --- | --- | --- |
| Batch | All analytes | Once per day or up to 20 samples | N/A |
| Blank | Combined or both TKN & NO3/NO2 individually | One per batch | < MRL |
| Standard | Combined or both TKN & NO3/NO2 individually | One per batch | Manufacturers recoveries, but not to exceed 80-120% Rec |
| Sample Spike | Combined or both TKN & NO3/NO2 individually | One per batch | 80-120% Rec |
| Sample Spike Duplicate | Combined or both TKN & NO3/NO2 individually | One per batch | 80-120% Rec and <20% RPD |
| QCS | Combined or both TKN & NO3/NO2 individually | One per batch or at least quarterly | Manufacturers recoveries, but not to exceed 80-120% Rec |
| Control Charts (Standard, QCS) | Combined or both TKN & NO3/NO2 individually | Establish control charts with warning limits (+2 sigma) and control limits (+3 sigma) | Update control charts after each set of samples – must be within control limits |

Please contact the Division of Water Laboratory Certification Program

for any additional information or clarification